## Slide 1: Cognitive Radio Spectrum Sensing and Allocation: A Low-Complexity Deep Learning Approach
Presented By:
Hamza Ahmed Abushahla, 90279
Ghanim Abdulla Alarai Al-Ali, 89804
Sultan Khalid Abdalla, 89987
Muhammad Ismail Sadaqat, 90340
Advised By:
Dr. Mohamed AlHajri
Dr. Taha Landolsi
COE491 Senior Design Presentation
Notes: Hamza

## Slide 2: Table of Contents
Motivation
Design Objectives
Literature Review
Implementation
Problem Statement
Conclusion
System Testing and Validation
Future Work
Notes: Hamza

## Slide 3: Problem Statement
Exponential growth of mobile and IoT devices
Unprecedented demand for radio frequency (RF) spectrum [1]
Pushing 4G and 5G bands to their limits [1]
Licensed spectrum bands often underutilized [5]
Congestion, interference, and performance issues
Spectrum scarcity threatens communication system efficiency [7]
Notes: Hamza

## Slide 4: Motivation
Cognitive radio (CR) is a significant and active research topic (Approx. 30K Publications)
Deep learning (DL) improves spectrum sensing (SS)
Adapts to various spectral patterns and interference
Intersects with embedded Machine Learning (ML), energy-efficient computing, and sustainability
Notes: Ghanim

## Slide 5: Literature Review
SS Approaches [8, 9]
Conventional SS techniques
ML-based SS: Supervised & Unsupervised
DL-based SS: Convolutional Neural Networks (CNNs)
CR Fundamentals [7, 10]
Spectrum holes concept
CR Networks: Centralized & Distributed
RF spectrum users: Primary Users (PUs) & Secondary Users (SUs)
Fig. 1. Spectrum hole concept [7]
Fig. 2. CR networks within a primary network [10]
Notes: Ghanim

## Slide 6: Literature Review
Hardware Platforms [42, 43]
Low-cost and efficient hardware platforms for SS
Microcontrollers, RF transmitters, and USB-software defined radio (SDR)
Embedded ML and DL-based SS algorithms
Spectrum Allocation [35, 40]
Dynamic spectrum allocation (DSA) in centralized CR networks
Processes SU requests on a first-come-first-serve (FCFS) basis
Allocates spectrum holes to SUs based on real-time availability
Notes: -S.K

## Slide 7: Design Objectives
A low-complexity CNN-based algorithm for SS
Centralized CR network architecture
Queueing model for DSA
Hardware implementation to showcase algorithm in a practical scenario
Notes: -S.K

## Slide 8: Implementation: Hardware
Central node
PU node
SU node
RTL-SDR
RF Transceivers
Sensors
System Interface
Fig. 3. System block diagram
Notes: S.K

## Slide 9: Implementation: Software
  Frequency Division Multiple Access (FDMA)
  Control Channel: 440MHz
  In-phase & quadrature (I/Q) samples
  Compressed CNN-based SS algorithm
  DSA queue for SU spectrum utilization
Fig. 3. System block diagram
Notes: M.S

## Slide 10: Implementation: CNN-Based DL Model
Fig. 4. Network architecture of the CNN model
Notes: M.S

## Slide 11: Implementation: Model Training
Acquired “SDR Dataset” [43]
Non-synthetic dataset emulating real Wi-Fi communications
I/Q samples from four 5-MHz-wide channels (20 MHz total)
Captured using USRP N210 SDRs via GNU Radio
Dataset divided: 80% for training, 10% for validation, 10% for testing
Our Collected Dataset
300,000 I/Q samples from 433 MHz and 500 MHz
Captured through GNU Radio using two RTL-SDR antennas
Arduino devices acted as PU transmitters for four scenarios
Energy detection used to determine frequency occupancy
Dataset divided: 80% for training, 10% for validation, 10% for testing
Notes: Ghanim

## Slide 12: Implementation: Training, Validation, and Testing Results
Acquired “SDR Dataset”:
  Trained on 287,971 data samples over 15 epochs
    Achieved high accuracy of 98.54% with low loss of 0.0473
  Tested on separate set of 31,997 data samples
    Attained high accuracy of 93.73% with loss of 0.2255
Fig. 5. Accuracy plot on the acquired SDR dataset
Notes: M.S

## Slide 13: Implementation: Training, Validation, and Testing Results
Our Collected Dataset:
  Trained on 240,000 data samples over 15 epochs
    Achieved exceptional accuracy of 98.98% with loss of 0.0190
  Tested on distinct set of 60,000 data samples
    Achieved impressive accuracy of 96.43% with loss of 0.3057
Fig. 6. Accuracy plot on the collected dataset
Notes: M.S

## Slide 14: Implementation: Model Compression Results
Compression using post-training quantization
Reduces the number of bits required to represent model weights
Lowers memory complexity of DL model
Crucial for deployment on resource-constrained devices
Quantization achieved an 75% reduction in model size with no loss in accuracy
Model | Accuracy (%) | Size (MB)
Baseline (Float 32) | 93.73 | 4.23
Float 16 | 93.74 | 2.11
Float 8 | 91.74 | 1.06
TF Lite Float 16 | 93.77 | 2.02
Model | Accuracy (%) | Size (MB)
Baseline (Float 32) | 96.43 | 16.80
Float 16 | 96.43 | 8.40
Float 8 | 96.40 | 4.2
TF Lite Float 16 | 96.18 | 8.02
Table 1. Performance on the acquired SDR dataset
Table 2. Performance on the collected dataset
Notes: Hamza

## Slide 15: Implementation: Experimental Setup
Central Node
and Transceiver
RTL-SDR Dongle and 2 Antennas
PU1 Node
PU2 Node
SU1 Node
SU2 Node
DHT-11 Sensors
MQ-135 Sensors
Fig. 7. Hardware experimental setup

## Slide 16: Implementation: System Interface
Fig. 8. System interface showing PU and SU activity
Notes: Hamza

## Slide 17: Implementation: System Interface
Fig. 8. System interface showing PU and SU activity

## Slide 18: System Testing and Validation
Occupied Spectrum Scenarios:
Tested system response to single and simultaneous PU transmissions.
Verified DL model’s accuracy in identifying occupied channels.
Unoccupied Spectrum Scenarios:
Examined system’s handling of no PU activity and multiple SU requests.
Confirmed correct channel allocation by the central node.
Dynamic Changes in Spectrum Occupation:
Assessed system’s adaptability to sudden PU arrivals during SU transmissions.
Verified reallocation of channels based on DL model updates.
Notes: Hamza

## Slide 19: Conclusion
Develop an intelligent spectrum sensing and allocation system
Utilize advanced DL algorithms and CR techniques
Optimize utilization of available frequency bands
Translate research into a practical implementation
Spectrum scarcity is a growing challenge
Notes: Ghanim

## Slide 20: Future Work
Further refine and improve the DL-based SS and allocation system
Deploy it in real-world scenarios to validate and improve its performance
Explore other DL-based architectures and optimization techniques
Adapt the DL-SS system to meet the demands of future 6G networks
Notes: -S.K

## Slide 21: Thank you for listening!